MUX
--implementazione di un Multiplexer a due bit

entity Mux is
--a e b ingressi, s selettore,r risultato
port(a,b,s: in bit;
r: out bit);
end Mux;

architecture MX of Mux is
begin

r <= ( a and (not s) ) or (b and s);
end MX;

CARRY LOOK AHEAD

--Implementazione del Carry Look Ahead a 4 bit

Entity carrylookahead is

port( a,b: in bit_Vector(3 downto 0);
 cin: in bit;
 s: out bit_Vector(3 downto 0);
 cout: out bit);

end carrylookahead;

Architecture CarryLookAhead4bit of carrylookahead is

signal p,g: bit_vector(3 downto 0);
signal c : bit_vector(3 downto 0);

begin

--generate g = a and b
g(0) <= a(0) and b(0);
g(1) <= a(1) and b(1);
g(2) <= a(2) and b(2);
g(3) <= a(3) and b(3);
--propagate p = a xor b;
p(0) <= a(0) xor b(0);
p(1) <= a(1) xor b(1);
p(2) <= a(2) xor b(2);
p(3) <= a(3) xor b(3);

--carry

c(0) <= cin;
c(1) <= (g(0) or (c(0) and p(0)));
c(2) <= (g(1) or((g(0) or (c(0) and p(0))) and	p(1)));

c(3) <= (g(2) or ( (g(1) or((g(0) or (c(0) and	p(0))) and p(1))) and p(2)));

cout <= (g(3) or ( (g(2) or ( (g(1) or((g(0)	or (c(0) and p(0))) and p(1))) and	p(2))) and p(3))) ;

--somma s(i-esima) = p(i-esimo) xor c(i-esimo-1)
s(0) <= p(0) xor c(0);
s(1) <= p(1) xor c(1);
s(2) <= p(2) xor c(2);
s(3) <= p(3) xor c(3);

end CarryLookAhead4bit;

CARRY SELECT

--Implementazione Carry Select ad otto bit
Entity CarrySelect8 is

--ingressi A(0:7), B(0:7), cin
--uscite: cout, S(0:7)
port(
a,b : in bit_Vector(7 downto 0 );
cin : in bit;
s : out bit_Vector(7 downto 0);
cout : out bit
);
end CarrySelect8;

Architecture CS8b of CarrySelect8 is

signal s0,s1 : bit_Vector(3 downto 0);
signal c0,c1,ci : bit;

--inclusione dei componenti CarryLookAhead a 4 bit
component carrylookahead is

port( a,b: in bit_Vector(3 downto 0 );
 cin: in bit;
 s: out bit_Vector(3 downto 0 );
 cout: out bit
 );
end component;

--inclusione dei componenti del Mux a 2 bit
component Mux is

port(a,b,s: in bit;
r: out bit
);
end component;
begin
--operazione dei Carry Look Ahead

CLAI : carrylookahead port map(a(3 downto 0 ),b(3 downto 0 ),cin,s(3 downto 0 ),ci);

CLA0 : carrylookahead port map(a(7 downto 4),b(7 downto 4),'0',s0,c0);

CLA1 : carrylookahead port map(a(7 downto 4),b(7 downto 4),'1',s1,c1);

--operazioni dei Mux
M4 : Mux port map(s0(0),s1(0),ci,s(4));
M5 : Mux port map(s0(1),s1(1),ci,s(5));
M6 : Mux port map(s0(2),s1(2),ci,s(6));
M7 : Mux port map(s0(3),s1(3),ci,s(7));
-- mux che calcola il riporto finale
MC :Mux port map(c0,c1,ci,cout);

end CS8b;

SIMULAZIONE

--file di testing per il CarrySelect ad 8 bit con almeno dieci coppie di operanti

--definizione dell'entita' astratta
Entity TestCarrySelect8 is
--entity astratta e percio' vuota
end TestCarrySelect8;

--definizione dell'architettura
Architecture SimCS8b of TestCarrySelect8 is
--si richiama il componente da utilizzare
component CarrySelect8 is

port(
a,b : in bit_Vector(7 downto 0);
cin : in bit;
s : out bit_Vector(7 downto 0);
cout : out bit
);
end component;

--si definiscono i segnali che si vogliono usare per l'utilizzo del componente

--ingressi
signal ia,ib: bit_Vector(7 downto 0);
signal icin : bit;
--uscite
signal os: bit_Vector(7 downto 0);
signal ocout: bit;

begin

--implementazione del circuito denominato tale(nella dichiarazione del componente)

circuito : CarrySelect8

port map(ia,ib,icin,os,ocout);

process
--si instanzia il componente
begin

--si devono assegnare dei valori che i segnali di	ingresso devono assumere negli istanti di tempo
considerati
--gli ingressi sono vettori!

--PRIMA COPPIA:inizializzazione a zero
ia<="00000000";ib<="00000000";
icin<='1';	--risultato= 0 0000 0001
wait for 10 ns;

--SECONDA COPPIA:inizializzazione ad uno
ia<="11111111";ib<="11111111";
icin<='0';	--risultato 1 1111 1110
wait for 15 ns;

--TERZA COPPIA
ia<="00001111";
icin<='1';	--risultato 1 0000 1111
wait for 10 ns;

--QUARTA COPPIA: bit alternati
ia<="01010101";ib<="10101010";
icin<='0';	--risultato 0 1111 1111
wait for 15 ns;

--QUINTA COPPIA:
icin<='1';	--risultato 1 0000 0000
wait for 10 ns;

--SESTA COPPIA
ia<="10000001";ib<="00001000";
icin<='0';	--risultato 0 1000 1001
wait for 15 ns;

--SETTIMA COPPIA
ia<="00011000";ib<="00000111";
icin<='1';	--risultato 0 0010 0000
wait for 10 ns;

--OTTAVA COPPIA
ia<="01111111";ib<="00000000";
icin<='1';	--risultato 0 1000 0000
wait for 15 ns;

--NONA COPPIA
ia<="11101010";ib<="01110101";
icin<='1';	--risultato 1 0110 0000
wait for 10 ns;

--DECIMA COPPIA
ia<="00000001";ib<="00000001";
icin<='1';	--risultato 0 0000 0011
wait for 15 ns;

--UNDICESIMA COPPIA
ia<="10000000";ib<="10000000";
icin<='0';	--risultato 1 0000 0000
wait for 10 ns;

--si conclude il processo
end process;

--si conclude la simulazione
end SimCS8b;